## Slide 1: The Risks of Lawn Pesticides
Jonathan Newman
Senior Pesticides Policy Advisor
The Environment Agency
The Risks of Lawn Pesticides
Issues and Mitigation Measures

## Slide 2
Credit UK Lawn Care Association

## Slide 3: Why Do They Matter?
Surface and Groundwater Pollution
Exceed the Environmental Quality Standard
Very Popular and used in large quantities
Over-applied
Hazardous

## Slide 4: Pesticides of Concern
Compound | Tonnes used per annum | PNEC | Human Health | AOEL
2,4-D | ? | 0.60 | Endocrine Disruptor, Reproduction Effects, Neurotoxicant, Respiratory and Eye Irritant WHO: Moderately Hazardous | 0.15 (12 mg)
Dicamba | ? | 2.2 | Respiratory and Eye Irritant WHO: Moderately Hazardous | 0.07 (5.6 mg)
Fluroxypyr | ? | 0.66 | Neurotoxin, Kidney toxicant Unlikely to present an acute hazard | 0.8 (64 mg)
Mecoprop P | ? | 0.10 | Reproduction effects, respiratory and eye irritant, Possible kidney & liver toxicant some evidence to suggest possible human carcinogen | 0.04 (3.2 mg)
https://pusstats.fera.co.uk/api/report-download/689
*Acceptable Operator Exposure Level - Systemic (mg kg⁻¹ bw day⁻¹)
Notes: Pesticide use survey
Lawn care 25 responses, 16 of which with pesticide data attached
Lawn care has shown a positive response in terms of the numbers received and one of the major lawn care companies not only submitted a response for their whole company (over 100 franchises), but also actively encouraged their franchisees to participate as well. Another smaller company provided information for each of their locations.

## Slide 5: 2,4-D
2,4-D is a selective, systemic herbicide used for the control of broad-leaved weeds. It is highly soluble in water, volatile and has a low potential to leach to groundwater based on its chemical properties.
It is non-persistent in soil but may persist in aquatic systems under certain conditions for up to 6 months.
It is moderately toxic to mammals but should not bioaccumulate. It may have negative effects on reproduction, development and is a neurotoxin and an irritant.
It is moderately toxic to birds and most aquatic species as well as honeybees and earthworms
Moderate risk of inhalation and dermal exposure depending on personal protection clothing and equipment utilised

## Slide 6: 2,4-D and Mecoprop P
Ecological Risk
  ERI scores of 3397 (6) and 1723 (9)
  Detected in 56% and 89% of samples
Human Health Risk
  Cumulative damage by repeated exposure
  Drinking water (removed by treatment)
  Endocrine disruptor, liver and kidney toxicant, reproductive and possible carcinogen

## Slide 7: Frequency of detection of 2,4-D in England

## Slide 10: Mecoprop P concentration

## Slide 11: Practical Measures to limit pesticide application to Lawns
Worse
  General application to lawn of mixed weed and feed
  Spray whole lawn with liquid pesticide
  Rinse containers down the drain
Better
  Spot treatment of weeds
  Dig out large weeds
  Rinse empty containers into the sprayer
  Any suggestions?

## Slide 12: Summary
Protect yourselves
Protect the environment